## Slide 1: MIPS Assembly Programming Language Part I
Ayman Hajja, PhD

## Slide 2: The Von Neumann Architecture
Memory holding both data and program (bytes)
Program |  |  | 
Data |  |  | 
Processor
Control Unit
Arithmetic Logic Unit
Address
bus
Data
bus

## Slide 3: Levels of Representation
High Level Language (e.g. C)
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
Assembly Language Program (e.g. MIPS)
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Machine Language Program (MIPS)
0000 1001 1001 0110 1010 1111 0101 1000
1111 1001 0000 1001 0000 1010 1111 0101
1001 1010 1111 0101 1000 1010 1111 0101
1001 1001 1010 1111 0101 1000 1010 1111
Compiler
Assembler

## Slide 4
Assembly language is a low-level programming language for a computer or other programmable device
Each assembly language is specific to a particular computer architecture, which is not the case for high-level programming languages
  Each family of processor chip (MIPS, PIC, SPARC, Alpha, Motorola, Intel, et al.) has its own architecture
  Each type of processor has its own assembly language.
Assembly Language

## Slide 5
Assembly language is converted into executable machine code by a program referred to as an assembler
In pure assembly language, one assembly language statement corresponds to one basic operation of the processor.
Assembly Language

## Slide 6
The MIPS chip was designed from the ground up in 1985.
MIPS Technologies (formerly MIPS Computer Systems) is a semiconductor company that built one of the first commercial RISC architectures.
Reduced Instruction Set Computer
Why MIPS instead of Intel x86?
    MIPS is simple, elegant. Don’t want to get bogged down in gritty details.
MIPS Assembly Language

## Slide 7: MEMORY ADDRESSES ARE IN BYTES
8 bit chunk of bits is called a byte
    1 word is 4 bytes
Word addresses are 4 bytes apart (more on that in future)
To say that memory is byte-addressable simply means that, given an "address", this address refers to a single block of 8 bits (or a byte)

## Slide 8: BASIC MACHINE CODE
The machine cycle of most processor chips looks like the following:
  Fetch the Instruction. The instruction is fetched from memory. The program counter contains the address of the instruction in memory.
  Increment the Program Counter. The program counter now points to the next instruction.
  Execute the Instruction. The operation asked for by the current machine instruction is performed.
      On a 32-bit processor, memory addresses are 32 bits wide and so the program counter (PC) holds a 32 bit address.

## Slide 9: MEMORY ADDRESSES ARE IN BYTES
Processor
Datapath
Registers
ALU
Memory
Enable?
Read/Write
Address
Read Data
Write Data
PC
Control