## Slide 1: MIPS ASSEMBLY PROGRAMMING LANGUAGE PART II
Ayman Hajja, PhD

## Slide 2: MEMORY ADDRESSES ARE IN BYTES
Processor
Datapath
Registers
ALU
Memory
Enable?
Read/Write
Address
Read Data
Write Data
PC
Control

## Slide 3: REGISTERS
Unlike C or Java, assembly does not use variables
Assembly operands are registers:
  Limited number of special locations built directly into the hardware
  Operations can only be performed on registers
Since registers are are directly built in the CPU, they are very fast (100 to 500 times faster than main memory)

## Slide 4: REGISTERS
Since registers are directly built in the CPU, there is a predetermined number of them:
    In MIPS, we have 32 general-purpose registers, and few other special-purpose registers

## Slide 5: REGISTERS
Registers are numbered from 0 to 31
Each register can be referred to by a number or name
Number references:
    $0, $1, $2, …, $30, $31
For now:
    $16 to $23 will be referred to by $s0 to $s7 (variables)
    $8 to $15 will be referred to by $t0 to $t7 (temp variables)
In general, use names to make your code more readable

## Slide 6: MACHINE INSTRUCTIONS
A machine instruction is a pattern of bits that directs the processor to perform one machine operation.
Here is the machine instruction that directs the MIPS processor to add two 32-bit registers together (a register is a part of the processor that holds a bit pattern).
0 0 0 0 0 0 0 1 0 0 1 0 1 0 1 1 1 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0
Means addition
# of the first register to add
# of the second register to add
Destination/Result register

## Slide 7: MIPS INSTRUCTIONS: ADD (REGISTER INSTRUCTION)
Addition in Assembly:
  Example 1: add $s0, $s1, $s2 (in MIPS)
  Equivalent to a = b + c; (in C), assuming that:
      $s1 contains the value of b
      $s2 contains the value of c
      and $s0 will be used to store the result (equivalent to 'a')

## Slide 8: MIPS INSTRUCTIONS: ADD (REGISTER INSTRUCTION)
Addition in Assembly:
  Example 1: add $s0, $s1, $s2 (in MIPS)
  Equivalent to a = b + c; (in C), assuming that:
      $s1 contains the value of b
      $s2 contains the value of c
      and $s0 will be used to store the result (equivalent to 'a')
  Example 2: add $s0, $s1, $zero (in MIPS)
  Equivalent to f = g; (in C), assuming that $s0 corresponds to f, and $s1 corresponds to g

## Slide 9: MIPS INSTRUCTIONS: SUB (REGISTER INSTRUCTION)
Subtraction in Assembly:
  Example: sub $s3, $s4, $s5 (in MIPS)
  Equivalent to: d = e - f; (in C), assuming that:
      d corresponds to $s3
      e corresponds to $s4
      f corresponds to $s5

## Slide 10: MIPS INSTRUCTIONS: ADDITION AND SUBTRACTION OF INTEGERS
How to do the following C statement?
          a = b + c + d - e;
a | $s0
b | $s1
c | $s2
d | $s3
e | $s4

## Slide 11: MIPS INSTRUCTIONS: ADDITION AND SUBTRACTION OF INTEGERS
a | $s0
b | $s1
c | $s2
d | $s3
e | $s4
How to do the following C statement?
          a = b + c + d - e;
We break it into multiple instructions:
    add $t0, $s1, $s2 # temp = b + c

## Slide 12: MIPS INSTRUCTIONS: ADDITION AND SUBTRACTION OF INTEGERS
How to do the following C statement?
          a = b + c + d - e;
We break it into multiple instructions:
    add $t0, $s1, $s2 # temp = b + c
    add $t0, $t0, $s3 # temp = temp + d
a | $s0
b | $s1
c | $s2
d | $s3
e | $s4

## Slide 13: MIPS INSTRUCTIONS: ADDITION AND SUBTRACTION OF INTEGERS
How to do the following C statement?
          a = b + c + d - e;
We break it into multiple instructions:
    add $t0, $s1, $s2 # temp = b + c
    add $t0, $t0, $s3 # temp = temp + d
    sub $s0, $t0, $s4 # a = temp - e
a | $s0
b | $s1
c | $s2
d | $s3
e | $s4

## Slide 14: IMMEDIATES
Immediates are numerical constants that are embedded in the instruction itself
Add Immediate:
addi $s0, $s1, -10 (in MIPS)
f = g - 10; (in C)
assuming $s0 and $s1 are associated with the variables f, g respectively