## Slide 1: Chapter 2: Instructions: Language of the Computer 2.1 – 2.3 Introduction, Operations and Operands, 2.4 – 2.5 Signed and Unsigned Numbers, Representing Instructions in the Computer ITSC 3181, Introduction to Computer Architecture https://passlab.github.io/ITSC3181/
Department of Computer Science
Yonghong Yan
yyan7@uncc.edu
https://passlab.github.io/yanyh/

## Slide 2: Chapter 2: Instructions: Language of the Computer
Lecture
  2.1 Introduction
  2.2 Operations of the Computer Hardware
  2.3 Operands of the Computer Hardware
Lecture
  2.4 Signed and Unsigned Numbers
  2.5 Representing Instructions in the Computer
Lecture
  2.6 Logical Operations
  2.7 Instructions for Making Decisions
☛
Lecture
  2.8 Supporting Procedures in Computer Hardware
  2.9 Communicating with People
  2.10 RISC-V Addressing for Wide Immediate and Addresses
Lecture
  2.11 Parallelism and Instructions: Synchronization
  2.12 Translating and Starting a Program
    We covered before along with C Basics
  2.13 A C Sort Example to Put It All Together
  2.14 Arrays versus Pointers
    We covered most before along with C Basics
  2.15 Advanced Material: Compiling C and Interpreting Java
  2.16 Real Stuff: MIPS Instructions
  2.17 Real Stuff: x86 Instructions
  2.18 Real Stuff: The rest of RISC-V
  2.19 Fallacies and Pitfalls
  2.20 Concluding Remarks
  2.21 Historical Perspective and Further Reading

## Slide 3: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction

## Slide 4: RISC-V and X86_64 Assembly Example

## Slide 5: The RISC-V Instruction Set
Used as the example throughout the book
  We will use and study only three classes of instructions for a handful of ins
  Sufficient for most programs.
Developed at UC Berkeley as open ISA
Now managed by the RISC-V Foundation (riscv.org)
Typical of many modern ISAs
  See RISC-V Reference Data tear-out card
Similar ISAs have a large share of embedded core market
  Applications in consumer electronics, network/storage, cameras, printers, …
Other Instruction Set Architectures:
  X86 and X86_32: Intel and AMD, main-stream desktop/laptop/server
  ARM: smart phone/pad
  RISC-V: emerging and free ISA, closer to MIPS than other ISAs
    The same textbook in RISC-V version
  Others: Power, SPARC, etc

## Slide 6: We Will Study Three Classes of Instructions
General form:
  <op word> <dest operand> <src operand 1> <src operand 2>
Arithmetic-logic instructions
  add, sub, addi, and, or, shift left|right, etc
Memory load and store instructions
  lw and sw: Load/store word
  ld and sd: Load/store doubleword
Control transfer instructions (changing sequence of instruction execution)
  Conditional branch: bne, beq
  Unconditional jump: j (
  Procedure call and return: jal and jr

## Slide 7: Components of a Computer
Input
Output
CPU or Processor
Notes: CPU or Processor

## Slide 8: Arithmetic Operations (of the First Class Instrs)
Add and subtract, three operands
  Two sources operands: provide input or source data
  One destination operand: where result goes to.
add a, b, c //sum of b and c is placed in a
All arithmetic operations have this form
  Three operands, two sources and one destination
  3-operands instructions
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware

## Slide 9: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled RISC-V code:
add t0, g, h // temp t0 = g + h add t1, i, j // temp t1 = i + j sub f, t0, t1 // f = t0 - t1
What are those symbols (t0, g, h, …) and where are their values are stored?
  Recall variables refers to memory locations
  Registers: super-fast small memory/storage used inside a CPU chip

## Slide 10: Registers in CPU
Registers are super-fast small memory/storage used in CPU.
  General-purpose registers, program counter, instruction register, status register, floating-point register, etc
  32 GP Registers in RISC-V CPU, 32-bit or 64-bit size for each
Data and instructions need to be loaded to memory and then register in order to be processed.
§2.3 Operands of the Computer Hardware

## Slide 11: Register Operands
Arithmetic instructions use register operands
  add <dest>, <src1>, <src2>
64-bit RISC-V has 32 64-bit general purpose registers
  The storage for all GP registers is called a register file
    It is storage, i.e. to store data
  Use for frequently accessed data
  Numbered x0 to x31
    the “memory address” for register
  64-bit data is called a ”doubleword”
  32-bit data called a “word”
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations

## Slide 12: RISC-V 32 64-Bit Registers, x0 to x31
Usage convention for most programs:
  x0: the constant value 0
  x1: return address of a function
  x2: stack pointer of a functon
  x3: global pointer
  x4: thread pointer
  x5 – x7, x28 – x31: temporaries
  x8: frame pointer
  x9, x18 – x27: saved registers
  x10 – x11: function arguments/results
  x12 – x17: function arguments
Notes: 32 64-bit registers are numbered x0 to x31
  Assembler names (alias) of some registers
    $t0, $t1, …, $t9 for temporary values
    $s0, $s1, …, $s7 for saved variables

## Slide 13: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j values are already loaded in x19, x20, …, x23
Compiled RISC-V code, all are register operands
  Three operands: the first operand is destination, last two are source operands
add x5, x20, x21 // x5 = x20 + x21 add x6, x22, x23 // x6 = x22 + x23 sub x19, x5, x6 // x19 = x5 – x6

## Slide 14: Second Class Instr: Memory Access
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
RISC-V is Little Endian
  Least-significant byte at least address of a word
  c.f. Big Endian: Most-significant byte at least address
To store number 12345678
Notes: To store number 12345678

## Slide 15: Memory Access Example
C code:
double A[N]; //double size is 8 bytes
A[12] = h + A[8];
  h in x21, base address of A in x22
Compiled RISC-V code:
  Index 8 requires offset of 64
  A[8] right-val, A[12]: left-val
ld x9, 64(x22) // load doubleword add x9, x21, x9 sd x9, 96(x22) // store doubleword
64(x22) and 96(x22) are memory operands, in contrast to register operands (x9)

## Slide 16: Load and Store Instructions
Format: ld rd, offset(rs1)
Example: ld x9, 64(x22) // load doubleword to x9
ld: load a doubleword from a memory location whose address is specified as rs1+offset (base+offset, x22+64) into register rd (x9)
  Base should be stored in an register, offset MUST be a constant number
  Address is specified similar to array element, e.g. A[8], for ld, the address is offset(base), e.g. 64(x22)
Format: sd rs2, offset(rs1)
Example: sd x9, 96(x22) // store a doubleword
sd: store a doubleword from register rs2 (x9 in the example) to a memory location whose address is specified as rs1+offset(base+offset, x22+96). Offset MUST be a constant number.
Load and store are the ONLY two instructions that access memory
lw: load a word from memory location to a register
sw: store a word from a register to a memory location

## Slide 17: More Load/Store Examples: Addressing Memory
int A[100]; base address (A, or &A[0]) is in x23, int is 4 bytes
Format: lw rd, offset(rs1)
Example: lw x6, 16(x23) // load word from A[4] to x6
Format: sw rs2, offset(rs1)
Example: sw x7, 32(x23) // store a word from x7 to A[8]
L/S A[0]: address can be specified as 0(x23).
A scalar variable (e.g. int f;) can be considered as one-element array (e.g. int f[1]) for load/store its value between mem and reg
  L/S a variable’s (e.g. int f) 32-bit value stored in a specific memory address which is stored in register x6 to register x8
    lw x8, 0(x6) //offset is 0
    sw x8, 0(x6)

## Slide 18: A[8] = A[10], base is in x23, each element 4 bytes
Lw x6, 40(x23)
Sw x6, 32(x23)
The context of the terms we use: base and offset
  For array/variable: base: &A[0], offset: bytes between A[0] and A[i];
  For LW/SW: base: base register, offset: the constant in the instr
  If you have address of A[4] in x9
    LW x5, 0(x9): load A[4]
    SW x5, 8(x9): store to A[6]
    SW x5, -8(x9): store to A[2]
Lab 02 helps you step-by-step for address

## Slide 19: More Load/Store Examples: Addressing Memory B[i], i is NOT constant
int B[N], B2[N]; // int type, 4 byptes
B2[i] = B[i];
Base address for B and B2 are in register x22 and x23. i is stored in register x5
  We need load B[i] to a register, e.g. x9, and then store x9 to B[2]
  Need to use the address for B[i] and B2[i] in load and store
    base+offset: B+i*4, and B2+i*4
  But i*4 is not constant, cannot be the offset of load and store
  Solution: Calculate the address of B[i] and B2[i] and store in registers as base for LW/SW, and then use 0 as offset in L/S
  slliw x6, x5, 2 // x6 now store i*4, slliw is i<<2 (shift left logic)
  add x7, x22, x6 // x7 now stores address of B[i].
  lw x9, 0(x7) // load a word from memory location (x7+0), which is B[i], into
  // reg x9
  add x8, x23, x6 // x8 now stores the address of B2[i]
  sw x9, 0(x8) // store a word from register x9 to memory location (x8+0)
  // which is B2[i]

## Slide 20: Registers vs. Memory
Registers are faster to access than memory
  ~100x faster, ~10 more expensive, and takes more space
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!

## Slide 21: Constant or Immediate Operands
Constant data specified in an instruction
addi x22, x22, 4
No subtract immediate instruction
  Just use a negative constant
  addi x2, x1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction

## Slide 22: The Constant Zero
RISC-V register x0 is the constant 0 always
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add x9, x5, x0
  addi x9, x5, 0

## Slide 23: Two Classes of Instructions so Far
Arithmetic instructions
  Three operands, could be either register or immediate (for source operands only)
    add x10, x5, x6; sub x5, x4, x7
    addi x10, x5, 10;
Load and store (L/S) instructions: Load data from memory to register and store data from register to memory
  Remember the way of specifying memory address (base+offset)
  ld x9, 64(x22) // load doubleword sd x9, 96(x22) // store doubleword
With these two classes instructions, you can implement the following high-level code, and different ways of combining them
  f = (g + h) - (i + j);
  A[12] = h + A[8];
  For L/S: Left-value (of =) to Store, Right-value of (=) to Load

## Slide 24: Psuedo-instructions Used in RARS
Are NOT machine instructions
Are assembly instructions that help programmers
  Translated to machine instructions by assembler
For example
  mv x6, x7 //move/copy value from x7 to x6
    Machine instruction: add x6, x7, x0 //since x0 is always 0
    Machine instruction: addi x6, x7, 0
  li x8, 100 //set the value of a register to be an immediate (load immediate)
    Machine instruction: addi x8, x0, 100
  la x10, label //load address of label to register
    Need two machine instructions
      auipc x8, xxx
      addi x0, x0, xxx

## Slide 25: Clarifying the Terms
For ALU to access register
  Fetch and set
For move data between mem and register
  Load and store
For move data between storage and mem
  Read and write
Storage

## Slide 26: Chapter 2: Instructions: Language of the Computer
Lecture
  2.1 Introduction
  2.2 Operations of the Computer Hardware
  2.3 Operands of the Computer Hardware
Lecture
  2.4 Signed and Unsigned Numbers
  2.5 Representing Instructions in the Computer
Lecture
  2.6 Logical Operations
  2.7 Instructions for Making Decisions
☛
Lecture
  2.8 Supporting Procedures in Computer Hardware
  2.9 Communicating with People
  2.10 RISC-V Addressing for Wide Immediate and Addresses
Lecture
  2.11 Parallelism and Instructions: Synchronization
  2.12 Translating and Starting a Program
    We covered before along with C Basics
  2.13 A C Sort Example to Put It All Together
  2.14 Arrays versus Pointers
    We covered most before along with C Basics
  2.15 Advanced Material: Compiling C and Interpreting Java
  2.16 Real Stuff: MIPS Instructions
  2.17 Real Stuff: x86 Instructions
  2.18 Real Stuff: The rest of RISC-V
  2.19 Fallacies and Pitfalls
  2.20 Concluding Remarks
  2.21 Historical Perspective and Further Reading

## Slide 27: Unsigned (Positive) Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
  3 digits for 000 to 111 (0 to 23-1)
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
§2.4 Signed and Unsigned Numbers

## Slide 28: Representing Signed (Positive and Negative) Numbers: Two’s Complement
The most significant bit indicates the sign (1 = negative, 0 = positive)
  0111: +710
  1010: -610
Positive numbers: SignMagnitude
  0111: +710
Negative numbers: Special, NOT SignMagnitude format
  1010 is -610, why it is “1 010”
  1110 is NOT -610 (110 is binary 6)
Given a 2’s-complement binary number, what is its decimal value:
  Look at the most significant bit for the sign of the number:
    1 = negative, 0 = positive
  Positive: most significant bit is 0, the absolute value is the value of the binary number
    0111 = +710, 0 is sign (+), 111 is 7, so it is +7
  Negative: most significant bit is 1, the absolute value is the inverted bits of the number + 1. inverting/flipping bit: 0  1, 1  0
    1010 = (-1) (0101+1) = (-1)(0110) = -610 (inverting 1010 yields 0101)
    1110 = (-1) (0001+1) = (-1) (0010) = -210

## Slide 29: What is the decimal value of the two’s complement number 10012?
Two’s Complement Examples
10012 is negative,
For the absolute value: invert it, which is 0110, and then plus 1:
0110
+ 1
01112 = 710, so 10012 = -710
For computer, the value of a 2’s complement number can be calculated using regular position binary form recognizing the sign bit
  1001 = (-1) * 23 + 0 + 0 + 1*20 = -7

## Slide 30: Representing using 2’s-Complement Binary
Given a decimal number, what is its 2’s-complement binary representation?
Positive: its binary representation
  710 = 01112, most significant big MUST be 0 to indicate it is positive
Negative: invert bits of the binary representation of the absolute value of the number and add up 1
  -3 = xxxx2
  Flip bits of 310 (00112)
  = 1100
  + 1
  11012 = -310

## Slide 31: 2’s-Complement Binary Representation of -610
610 = 01102, then invert +1
1001
+ 1
10102 = -610

## Slide 32: Rang of Two’s Complement Numbers
4-digit 2’s-complment numbers:
  Most positive 4-bit number: 0111, 7
  Most negative 4-bit number: 1000, -8
    1111 is -1
  Range of an N-bit two’s comp number:
  [-(2N-1), 2N-1-1]

## Slide 33: 2’s-Complement Signed Integers (32 bits)
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
  Or do invert+1: -(0011+1) = -(0100) = -410
For 32 bits
  –2,147,483,648 to + 2,147,483,647

## Slide 34: 2s-Complement Signed Integers of 32 Bits
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
Range: [-(232-1), 232-1-1]
2n – 1 can’t be represented
  1000… is negative now
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000, which is –2,147,483,648
  Most-positive: 0111 1111 … 1111, which is 2,147,483,647
Notes:   to + 2,147,483,647

## Slide 35: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = +2 +1 = 0000 0000 … 00102 + 1 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102

## Slide 36: Add Two 2’s Complement Numbers: Just Bit-wise Addition
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers

## Slide 37: Add Two 2’s Complement Numbers: Just Bit-wise Addition, no need to recognize positive/negative number, easier to implement in hardware
Add 6 + (-6) using two’s complement numbers
Add -2 + 3 using two’s complement numbers

## Slide 38: Sign Extension
Representing a number using more bits
  E.g. char a = -5; int b = a;
    A char variable takes 1 byte of memory, and an int variable takes 4 bytes.
    How to fill in the bits of the 4 bytes of memory for an int variable with a 8-bit number?
  Preserve the numeric value
Replicate the sign bit to the left
  c.f. unsigned values: extend with 0s
  1011 (-5 with 4 bits)  1111 1011 (-5 in 8 bits char)
  11111011 (-5 in char)  11111111 11111111 11111111 11111011 (-5 in 32-bits int)
More examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110
In RISC-V instruction set
  addi: extend immediate value
  lb,lh,lw,ld: extend loaded byte/halfword/word/doubleword
  lbu, lhu, lwu, ldu: zero extend loaded byte/halfword/word/doubleword
  beq, bne: extend the displacement

## Slide 39: Three Classes of Instructions
Arithmetic-logic instructions
  add, sub, addi, and, or, shift left|right, etc
Memory load and store instructions
  lw and sw: Load/store word
  ld and sd: Load/store doubleword
Control transfer instructions (changing sequence of instruction execution)
  Conditional branch: bne, beq
  Unconditional jump: j (
  Procedure call and return: jal and jr

## Slide 40: Representing Instructions
Instructions are encoded in binary
  Using binary numbers to represent
  operations, operands, and immediate
  Called machine code
RISC-V instructions
  Each instruction is encoded as a 32-bit instruction word
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
Instructions use 32 registers:
  We need 5 bit to identify 32 registers (0 to 31)
  00000 to 11111
§2.5 Representing Instructions in the Computer

## Slide 41: Hexadecimal
Base 16 format to easily show binary number
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000

## Slide 42: RISC-V R-Format Instructions
R-Format: Operands are all from Registers
Arithmetic and logic instructions that use registers for ALL operands. Format: op rd, rs1, rs2.
Instruction fields
  opcode: operation code
  rd: destination register number
  funct3: 3-bit function code (additional opcode)
  rs1: the first source register number
  rs2: the second source register number
  funct7: 7-bit function code (additional opcode)
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
32 bits

## Slide 43: R-Format Encoding Example 1
add x9,x20,x21 (add rd, rs1, rs2)
x21, x20, x9 add
0000 0001 0101 1010 0000 0100 1011 0011two =
015A04B316
5 bits for rd, rs1 and rs2 because we have 32 registers, thus only needs 5 bit to address a register
0
21
20
9
0
51
0000000
10101
10100
01001
000
0110011
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits

## Slide 44: R-Format Encoding Example 2
add x6, x10, x6 (add rd, rs1, rs2)
x6, x10, x6 add
0000 0000 0110 0101 0000 0011 0011 0011two =
0065033316
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
0
6
10
6
0
51
0000000
00110
01010
00110
000
0110011
Opcode (51), funct3 (0) and funct7(0) for each instruction are defined by the ISA standard.

## Slide 45: R-Format Instruction Encoding http://content.riscv.org/wp-content/uploads/2017/05/riscv-spec-v2.2.pdf#page=116
RV32I Base Instruction Set
RV64I Base Instruction Set (in addition to RV32I)
Arithmetic instructions
Logic instructions

## Slide 46: RISC-V I-Format Instructions
I-Format: The second source operand is an Immediate, the first source operand is register, destination operand is register.
Immediate arithmetic/logic, and load instructions (NOT store instruction)
  addi x22, x22, 4; Format: addi rd, rs1, #immediate
  ld x9, 64(x22); Format: ld|lw, rd, #immediate(rs1)
  rs1: source or base address register number
  immediate: constant operand, or offset added to base address
    2s-complement, sign extended
  NOT for store: because destination for store is the memory location (not a register), thus no rd for store.
Design Principle 3: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits

## Slide 47: I-Format Instruction Encoding http://content.riscv.org/wp-content/uploads/2017/05/riscv-spec-v2.2.pdf#page=116
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits
Immediate arithmetic/logic
load instructions

## Slide 48: Shift Operation Encoding
Use immediate operands, I-Format
  Immediate: slli, sri, srai, etc
If use registers for all operands, R-Format
  Sll, sri, sra
rs1
rd
funct3
opcode
6 bits
7 bits
5 bits
5 bits
3 bits
funct6
immed
6 bits
funct7
rs2
rs1
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
rd

## Slide 49: RISC-V S-Format Instructions
S-Format: instructions that use two source register operands and NO destination operand register (rd), only store instruction
Format: sd|sw, rs2, #immediate(rs1)
Different immediate format for store instructions
  sd x9, 96(x22);
  rs1: base address register number (x22)
  rs2: source operand register number (x9), which provide the value to be stored to memory
  immediate: offset added to base address
    Split so that rs1 and rs2 fields always in the same place as for R- or I-Format
rs2
rs1
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
imm[11:5]
imm[4:0]

## Slide 50: S-Format Instruction Encoding http://content.riscv.org/wp-content/uploads/2017/05/riscv-spec-v2.2.pdf#page=116
rs2
rs1
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
imm[11:5]
imm[4:0]
Store instructions

## Slide 51: More Examples from Textbook 2.5

## Slide 52: More Examples from Textbook 2.5

## Slide 53: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture

## Slide 54: RISC vs. CISC
Design “philosophies” for ISAs: RISC vs. CISC
  CISC = Complex Instruction Set Computer
    X86, X86_64 (Intel and AMD, main-stream desktop/laptop/server)
    X86* internally are still RISC
  RISC = Reduced Instruction Set Computer
    ARM: smart phone/pad
    RISC-V: free ISA, closer to MIPS than other ISAs, the same textbook in RISC-V version
    Others: Power, SPARC, etc
Tradeoff:
RISC:
  Small instruction set
    Easier for compilers
  Limit each instruction to (at most):
    three register accesses,
    one memory access,
    one ALU operation
    => facilitates parallel instruction execution (ILP)
  Load-store machine: minimize off-chip access